## Slide 1: Lesson 9: Software Safety Basics

## Slide 2: Software and safety-critical systems
We are now using software in systems that we call safety-critical. These are systems that, if they fail, will have very serious consequences:
  nuclear reactor monitoring
  flight control systems
  software controllers on X-ray machines
Software Safety is a sub discipline of systems engineering that applies scientific, management, and engineering principals in insuring adequate safety throughout the system life cycle so that software’s produced are not defective but can live to their tasks

## Slide 3: Patriot missile defense system failure
On February 25, 1991, a Patriot missile defense system operating at Dhahran, Saudi Arabia, during Operation Desert Storm failed to track and intercept an incoming Scud. This Scud subsequently hit an Army barracks, killing 28 Americans. [GAO]
http://news.bbc.co.uk/1/shared/spl/hi/middle_east/03/v3_iraq_timeline/html/scuds.stm

## Slide 4: Patriot: A software failure
[A] software problem in the system’s weapons control computer… led to an inaccurate tracking calculation that became worse the longer the system operated.
At the time of the incident, the battery had been operating continuously for over 100 hours. By then, the inaccuracy was serious enough to cause the system to look in the wrong place for the incoming Scud. [GAO]

## Slide 5: Ariane 5 failure
On 4 June 1996, the maiden flight of the Ariane 5 launcher ended in a failure. Only about 40 seconds after initiation of the flight sequence, at an altitude of about 3700m, the launcher veered off its flight path, broke up and exploded.
http://www.vuw.ac.nz/staff/stephen_marshall/SE/Failures/SE_Ariane.html

## Slide 6: Ariane 5: A software failure
Unexpectedly large values encountered during alignment of “inertial platform”
Attempt to convert overly large 64-bit value into a 16-bit value
Software exception
Guidance system (hardware) shutdown

## Slide 7: Sources of the problem
Alignment code reused from
(smaller, less powerful) Ariane 4
  Velocity values of Ariane 5 were out of range of Ariane 4
Ironically, alignment not even needed after lift-off!
Why was alignment code running?
  Engineers decided to leave it running for 40 seconds after planned lift-off time –
  Permitting easy restart if launch was put on hold briefly

## Slide 8: What is software safety?
Features and procedures which ensure that
  a product performs predictably under normal and abnormal conditions, and
  the likelihood of an unplanned event occurring is minimized and its consequences controlled and contained;
thereby preventing accidental injury or death, whether intentional or unintentional. (Herrmann)

## Slide 9: Features and procedures
Features: built into the software itself
  Range checks; monitors; warnings/alarms
Procedures: concern the proper environment for the software, and its proper use
  Computer hardware that the software runs on
  Physical, mechanical components of environment
  Human users

## Slide 10: Normal and abnormal conditions
Abnormal conditions:
  Failure of hardware components
  Power outage
  Extreme environmental conditions (temperature, velocity)
What to do?
  Not necessarily the best reaction, but one that has the best chance of preventing injury or death
  Fail-safe: shut down
  Fail-operational: continue in “simpler” degraded mode

## Slide 11: Avoiding “unplanned events”
To Herrmann, human users are the primary source of such events
  Can produce unusual inputs or combinations of inputs
User interface design, testing can be crucial to software safety
  Understand user behavior
  Create interfaces that guide users toward “good” input

## Slide 12: Fault, error and failure
Fault: cause of error
- Misinterpreted software requirements
- Code defects: code doesn’t implement required behavior
Error: dangerous state,
from which failure is possible
Failure: unacceptable system behavior

## Slide 13: Fault, error and failure: Example
Fault: memory device fails
- Note: failure of component means fault at higher level
- If memory device not used, fault remains hidden
Error: attempt at memory access is unsuccessful
- Now, presence of fault is evident
- But, software may be able to handle it “gracefully”
Failure: unsuccessful memory access results in computing an “out of bounds” value

## Slide 14: Software Safety
Ensures software will execute within a system context without resulting in unacceptable risk
Safety-critical software functions
  Directly or indirectly allow a hazardous system state to exist
Safety-critical software
  Contains safety-critical functions

## Slide 15: System Safety
System Safety analysis method to . . .
  Identify hazards to system, mission, or element
  Assess severity, likelihood of occurrence, & consequences of each hazard on affected system elements
  Identify safety requirements & preferred designs.

## Slide 16: Mishap Severity Categories
Catastrophic – could result in death, permanent total disability, loss exceeding $1M, severe environmental damage violating law or regulation
Critical – could result in permanent partial disability, injuries or illness affecting at least 3 people, loss >$200K but <$1M, or reversible damage to environment but violating law or regulation
Marginal – could result in injury or illness resulting in loss of 1 or more work days, loss >$10K but <$200K, mitigatable environmental damage without violation of law or regulation where restoration activities can be accomplished
Negligible – Could result in injury or illness not resulting in lost workdays, loss >$2K but <$10K, minimal environmental damage not violating law or regulations

## Slide 17: Software Failure Causes
User Experiences
System Failure
During Operations
Users
Software
Misunderstanding
Requirements
Software
Design Error
Software
Implementation
Error
Hardware
Design
Error
Materials
Defect
Environmental
Effects & Stress
Caused by
Caused by
Caused by
Incorrect
Action
Incorrect
Usage
Incorrect Processing
Incorrect Response
Incorrect Computed Result
Performance Degradation
System Restart or Reboot
System Halt
Malware
Unauthorized
Access
* Note: some failures might look like failures caused by software. Need to be careful.

## Slide 18: Faults: Hardware vs. software
Some hardware faults may be random
  Due to manufacturing defects or simple “wear and tear”
  Probability can be estimated statistically
  Well-known techniques to minimize random faults:
  error-correcting codes, redundant systems
Software faults are always systematic – not random
  Generated during design or specification – not execution
  Software is not manufactured and doesn’t “wear out”
  Techniques for minimizing random faults don’t work with systematic faults
    Ariane 5 had redundant systems – all running the same software!

## Slide 19: Fault management options
Avoidance: Prevent faults from entering the system during the design phase
  “good practices” in design – e.g. programming standards
Removal: Find faults in the system before release
  Testing – costly and not always very effective

## Slide 20: Fault management options
Tolerance: Find faults in operational system after release, allow system to proceed correctly
  Recovery blocks:
    Create duplicate code modules
    Run “primary module”, then run an “acceptance test”
    If test fails, roll back changes and run an “alternative module”
  N-version programming:
    several independent implementations of a program
    Goal: ensure “design diversity”, avoid common faults
  Both approaches are costly, and may not be very effective
    For a study on whether N-version programming really achieves “design diversity”, read Knight & Leveson’s article.

## Slide 21: Address Software Safety
Address Software Safety in . . .
  Software Requirements and Design
  Software Processes and Methods
  Software Tools and Tooling
Software Safety
Requirements & Design
Processes & Methods
Tools & Tooling

## Slide 22: References
United States General Accounting Office. Report IMTEC-92-26, February 4, 1992. http://www.fas.org/spp/starwars/gao/im92026.htm
Ariane 5 Flight 501 Failure – Report by the Inquiry Board. July 19, 1996. http://sunnyday.mit.edu/accidents/Ariane5accidentreport.html
U.S. Nuclear Regulatory Commission. Update on radiation therapy overexposures in Panama. NRC Information Notice 2001-08, Supp. 2, November 20, 2001. http://www.hsrd.ornl.gov/nrc/special/IN200108s2.pdf
D. Gage and J. McCormick. Why software quality matters. Baseline, March 2004, 33-56. http://www.baselinemag.com/print_article2/0,1217,a=120920,00.asp
Nancy G. Leveson. Safeware: System Safety and Computers. Addison Wesley, 1995.
Neil Storey. Safety-Critical Computer Systems. Prentice Hall, 1996.
J.C. Knight and N.G. Leveson. An experimental evaluation of the assumption of independence in multiversion programming. IEEE Transactions on Software Engineering 12(1), 1986, 96-109.